## Slide 1: Averaging (or equalizing) level control
By Finn Aakre Haugen
(finn.haugen@usn.no)
Course IIA1117 Control Engineering Fall 2017

## Slide 2
2
Buffer tank with a level control system
Aim: Averageing (or equalizing, or attenuating) inflow variations so that the outflow becomes smoother than the inflow.

## Slide 3
3
How to tune LC?
We need a sluggish or soft or compliant LC so that the liquid volume (the level) can take up the inflow variations.
Ziegler-Nichols is useless here since it gives fast or stiff control :-(
But Skogestad is excellent, using Tc as tuning parameter :-)
Kc = 1/(Ki*Tc) Ti = 2*Tc
where
Ki = -1/A is the integrator gain or normalized process step response.
How to select Tc?
...

## Slide 4
4
...
How to select Tc?
As a start, assume P (proportional) level controller. It can be shown, from a mathematical model of the level control system, that
Δhmax = (Tc/A)*ΔFin
where Δhmax is corresponding maximum allowed level change (in steady state) after max inflow step change, ΔFin.
With a PI controller with the same Tc:
Δhmax <= (Tc/A)*ΔFin
Solving this inequality for Tc gives
Tc >= A* Δhmax/ΔFin
=> Specification of Tc in the PI settings:
Tc = A* Δhmax/ΔFin

## Slide 5
5
Comparison of responses in level h
due to step change in inflow Fin, with P and with PI controllers:

## Slide 6
6
Example
Assumptions:
A = 2000 m2
ΔFin = 1 m3/s
Δhmax = 0.5 m
Resulting Tc:
Tc = A* Δhmax/ΔFin = 2000*(-0.5)/(-1) = 1000 s
PI settings:
Kc = 1/(Ki*Tc) = -A/Tc = -2000 m2 / 1000 s = 2.0 (m3/s)/m
Ti = 2*Tc = 2*1000 s = 2000 s

## Slide 7
7
Simulation!