## Slide 1: Cascade control
By Finn Aakre Haugen
(finn.haugen@usn.no)
Course IIA1117 Control Engineering Fall 2017

## Slide 2
Benefit of cascade control (comparing with ordinary single loop control):
Faster (more effective) compensation of process disturbances.

## Slide 3
Review: Single-loop control system
3

## Slide 4
Improved structure with faster (more effective) disturbance compensation:
Cascade control system
4

## Slide 5
Interpretation: With cascade control, the original actuator
is substituted by a "new" well-behaving" actuator:

## Slide 6
Controller tuning:
First, tune the secondary controller (with the primary controller in Manual mode).
Then, tune the primary controller (with the secondary controller in Auto mode).

## Slide 7
  Example 1: Cascade control of temperature in a vessel
7
Simulator (unzip all the files, and then run the exefile).

## Slide 8
  Example 1 cont.: Comparing performance indexes IAE (Integral of Absolute value of control Error):
  Which of the control structures is the best?
  Cascade
  Single-loop
  Their ratio
  Excitation
  (Forstyrrelse = disturbance)
  (Sprang = step)

## Slide 9
  Example 2: Cascade control of heat exchanger
  Simulator