## Slide 1: Process dynamics
By Finn Aakre Haugen
(finn.haugen@usn.no)
Course PEF3006 Process Control Fall 2017
Lecture:
(Enter presentation mode of Powerpoint with the F5 key.)

## Slide 2: Terms
Why are these terms important?
To give names to dynamic properties of physical systems
To make you identify and understand dynamic properties
Can be used in controller tuning - using model-based methods (e.g. Skogestad’s method - to be described later in this course)
Gain
Time-constant
Integrator (or accumulator)
Time-delay

## Slide 3
Time-constant systems can be represented with the following differential equation, where u is the system input and y is the output:
Definition of time-constant systems
From this differential equation we can calculate the following transfer function from input u to output y:
T is the time-constant. K is the gain.
This transfer function is the standard transfer function of a time-constant system.

## Slide 4
K and T in the step response
By applying a step at the input of the system, you can read off K and T from
the step response at the output.
ys
U
t
Step response:
Input step
T is the 63% response time
K = Output / Input = ys/U = delta y / delta u
(at steady-state!)

## Slide 5
Simulator:
Time-constant

## Slide 6
Example: Liquid tank with heating
Simulator:
Heated tank
(Mathematical model on next slide.)

## Slide 7
Mathematical model of heated tank
Energy balance:
From this differential equation we can derive the following transfer functions, assuming neglected heat transfer (Uh=0) (Delta indicates “deviation from operating point”):
If the heat transfer is neglected (Uh=0), the time-constant is simply mass divided by mass flow:
Time-constant and gains:
Let's see if m/F is equal to the "experimental" time-constant as read off on the simulator: Heated tank

## Slide 8
Integrator systems can be represented with the following integral equation, where u is the system input and y is the output:
Definition of integrator systems
The above integral equation corresponds to this diff. equation:
Ki is the integrator gain.
The transfer function from input to output is
An integrator can be termed accumulator as it accumulates the inputs: y(tk) = Ki * [u(t0) + u(t1) + … + u(t0)]*dT

## Slide 9
Step response of an integrator
The step response is a ramp:
Input (step)
Output (ramp)

## Slide 10
  Simulators:
Integrator
Liquid tank
(Mathematical model on next slide.)

## Slide 11
Mathematical model of liquid tank
A * dh/dt = qin – qout = qin – Kp*up (pump)
Mass balance (assume valve is closed):
dh/dt = (1/A) * (qin – qout) = (1/A) * (qin –Kp*up)
which is on the standard form of an integrator
(except in our example we have two “input” signals, qin and qout)

## Slide 12: Time-delay (or transport-delay, dead-time)
Example: Conveyor belt
(Outflow is equal to time-delayed inflow.)
Transfer function:

## Slide 13
  Simulator:
Time-delay

## Slide 14
Very hard questions:
1.
2.

## Slide 15: Combined dynamics
Example: Wood-chip tank
Level control of wood-chip tank
How will you characterize
the dynamics of this system?