## Slide 1: Introduction to process control
By Finn Aakre Haugen
(finn.haugen@usn.no)
Course PEF3006 Process Control Fall 2017

## Slide 2: Software requirement for running SimView simulators
  Most of the lectures and exercises of this course include running simulators. These simulators have been developed in LabVIEW. Here are the requirements for the simulators to run.

## Slide 3
What is automatic control?

## Slide 4
  Automatic control is making process variables stay sufficiently near their setpoints (references)
  - automatically (i.e. without manual operations):

## Slide 5
Common process variables
to be controlled to follow setpoints:
Temperature (heat exchanger, reactor, room)
Pressure (reactor, oil/water/gas-separator)
Flow (gas or liquid flows in pipe)
Level (tank)
Position (ship, robot)
Rotational speed (motor)

## Slide 6
Product quality
Product economy
Safety
Environment protection
Comfort
Feasibility
Automation
Areas where automatic control
can make large benefits:

## Slide 7
The principle of feedback control

## Slide 8
Think about how you you act
while you are controlling the temperature of the water in the shower to make the temperature become equal to the desired temperature (aka. the temperature setpoint or reference), even under disturbances like reduced availability of hot water and variations of air temperature in the room.

## Slide 9
I guess you act like this (text on next slide):

## Slide 10
You manipulate the actuator (tap) until the difference between the temperature setpoint and the temperature measurement is sufficiently small.
This is error-driven control!
It is the fundamental control principle in technical, industrial, biological, social system.
More common terminology than error-driven control:
Feedback control
Closed loop control
Automatic control

## Slide 11
Temperature control system implemented with industrial components:

## Slide 12
(TT = Temperature Transmitter)
(TC = Temperature Controller)
Piping & Instrumentation Diagram (P&ID) for
the temperature control system:

## Slide 13
So, how does the controller act?
It manipulates the process variable by changing the control signal to the actuator
until the control error has become zero. So, it continually improves, until the aim is reached:
Zero error.
In practice it is the mean error which will be zero as there will always be some disturbances making the error vary somewhat, see the figure below.

## Slide 14
Example of industrial feedback control system:
Level control of wood chip tank
(Process & Instrumentation Diagram - P&ID)

## Slide 15
  Simulation!

## Slide 16
  Simulation:
Level control of wood-chip tank
(Run the exe-file in the link.)

## Slide 17
  Another example:

## Slide 18
  Simulator:
Temperature control of liquid tank

## Slide 19
A third industrial example: Dynamic positioning (DP) of ships
Kongsberg Maritime AS
Eng.: Disturbance
Eng.: Disturbance

## Slide 20
  Simulator

## Slide 21
  Symbols in
  Piping & Instrumentation Diagrams (P&IDs)

## Slide 22
Standards for P&IDs:
ISO 3511-1
ISA S5.1

## Slide 23
Letter codes (for P&IDs):

## Slide 24
Instrumentation symbols:

## Slide 25
Process fluid and signals:

## Slide 26
Valves:

## Slide 27
Tanks:

## Slide 28
Heat exchanger:

## Slide 29
Pumps:

## Slide 30
  Block diagrams of control systems

## Slide 31
A simplified block diagram showing the most essential parts:
We will relate this block diagram to the level control system of the wood-chip tank.