## Slide 1: On-Off Control (alternative to PID)
By Finn Aakre Haugen
(finn.haugen@usn.no)
Course PEF3006 Process Control Fall 2017

## Slide 2
2
  On-off controller function:
I think that the On-off controller is the simplest
error-based (or: feedback-based) controller that exists.
u = umax when e >= 0.
u = umin when e < 0.

## Slide 3
3
  On-off controller with dead-zone:
De is the dead-band. Purpose is to avoid control signal changes caused by measurement noise.

## Slide 4
4
  Comparison with P-controller:
P-controller:
u = Kp*e + u0
Kp
u0
On-off controller

## Slide 5
  Example: Temperature control with PID and On-off controller

## Slide 6
  Simulated responses:
  On-off pattern of control signal can cause problems with mechanical actuators, but not with electrical actuators.
  Process variable (temperature) varies around the setpoint, which is fine.
  But is the average control error zero (as we normally would like to obtain)?
  Process variable (temperature) oscillates!