## Slide 1: On-Off control
Course: Process Control, NMBU
Dec 2017 - April 2018
By Finn Aakre Haugen, PhD, TechTeach
(finnhaugen@hotmail.com)

## Slide 2
2
  On-off controller function:
I think that the On-off controller is the simplest
error-based (or: feedback-based) controller that exists.
u = umax when e >= 0.
u = umin when e < 0.

## Slide 3
3
  On-off controller with dead-zone:
De is the dead-band. Purpose is to avoid control signal changes caused by measurement noise.

## Slide 4
4
  Comparison with P-controller:
P-controller:
u = Kp*e + u0
Kp
u0
On-off controller

## Slide 5
  Example: Temperature control with PID and On-off controller

## Slide 6
  Simulated responses:
  On-off pattern of control signal can cause problems with mechanical actuators, but not with electrical actuators.
  Process variable (temperature) varies around the setpoint, which is fine.
  But is the average control error zero (as we normally would like to obtain)?
  Process variable (temperature) oscillates!